Facultatea Automatică Şi Calculatoare

Titlul tezei: Tehnici avansate de diagnoză cu aplicaţii în supravegherea parametrilor de mediu industrial

Autor: ing. Şimonca Ana Magdalena

Coordonator Ştiinţific: prof. dr. ing. Theodor Borangiu

Abstract

Poluarea  este una din marile probleme cu care se confruntă omenirea în condiţiile unei dezvoltări socio-economice pe termen lung.Această teză a fost realizată urmărind două obiective principale. Primul dintre ele îl constituie fundamentarea teoretică a proceselor fizice care stau la baza modelării calităţii aerului, iar cel de-al doilea obiectiv identificarea şi descrierea tehnicilor de diagnoză a stărilor de poluare chimică a atmosferei, determinată de diverse surse de origine antropică, folosind rezultatele măsurătorile practice ale distribuţiilor de concentraţii coroborate cu valorile prevăzute de Directivele Europene, modelarea fizico-matematică şi cea bazată pe inteligenţa artificială pentru predicţia calităţii aerului în zone urbane.

Rezultatele cercetărilor au fost utilizate pentru proiectarea şi realizarea reţelei de monotorizare a aerului în oraşul Bucureşti, dezvoltarea unui sistem de monitorizare a calităţii aerului şi alertare în mediul urban bazat pe datele obţinute de la o reţea de staţii mobile de măsurare montate pe vehiculele aparţinând reţelei de transport în comun,  dezvoltarea şi evaluarea modelelor bazate pe inteligenta artificiala pentru prognoza calitatii aerului şi analiza stării de poluare a aerului în Bucureşti, în perioada 2004-2011, pentru poluanţii monoxid de carbon, pulberi (sau particule) în suspesie, PM10 şi bioxid de sulf, emişi de surse specifice mediului urban: trafic, surse industriale, surse rezidenţiale, şantiere de construcţii

Pe baza informaţiilor privind gradul de poluare obţinute de la reţelele de monitorizare sau estimate folosid diverse tipuri de modele se pot elabora planuri strategice de asigurare a zonei de securitate în zonele urbane din jurul marilor surse de poluare  în eventualitatea producerii unui accident sau  se pot lua decizii privind  protecţia omului, societăţii şi mediului inconjurător în condiţii de functionare normala a obiectivelor  care emit poluanti în atmosferă.

Faculty of Automatic Control and Computer Science

Thesis title: Advanced Diagnosis Techniques with Applications in Environmental Monitoring Parameters

Author: eng. Şimonca Ana Magdalena

Scientific coordinator: prof. dr. ing. Theodor Borangiu

Abstract

Pollution is one of the biggest problems that the mankind is facing in terms of socio-economic development in the long run. This PhD thesis was carried out following two main objectives. The first one is to establish the theoretical basis for the physical processes underlying air quality modeling, and the second objective is to identify and describe diagnosis techniques for the state of chemical pollution of the atmosphere, caused by various sources of anthropogenic origin, using the results of measurements practical concentration distributions in conjunction with the values set by European Directives, mathematical and physical modeling based on artificial intelligence to predict air quality in urban areas.

Research results were used for design and implementation of  a monitoring network for  air  quality for Bucharest, development of an air quality monitoring and alerting in urban areas based on data from a network of mobile measuring stations mounted on vehicles belonging to the network transport, development and evaluation of models based on artificial intelligence and analysis to forecast air quality status of air pollution in Bucharest, between 2004-2011, for the pollutants carbon monoxide, particulate matter PM10 and dioxide sulfur emitted by specific sources urban traffic, industrial sources, residential sources, construction sites

Based on information obtained from pollution monitoring networks or using estimates from different types of models, strategic plans can be developed to ensure a security area around large urban pollution sources in the event of an accident or to make decisions for protection of man, society and the environment under normal operating conditions of the agents that emit pollutants into the atmosphere.