# Facultatea de energeticĂ

# ContribuŢii la elaborarea metodelor de decontaminare cu microunde a mediilor poluate

| Doctorand | Conducător de doctorat |
| --- | --- |
| Ing. Daniela IORDACHE | Prof. dr. ing. Nicolae GOLOVANOV |

# Preocupările intense din ultimile decenii pentru protejarea mediului înconjurător şi pentru limitarea emisiilor de gaze cu efect de seră au determinat dezvoltarea tehnologiilor de decontaminare „curate”, nepoluante pentru mediu. Tehnologiile cu microunde reprezintă o alternativă importantă datorită avantajelor pe care le prezintă faţă de tehnologiile clasice într-o gamă largă de aplicaţii, cele mai cunoscute fiind procesele de prelucrare a materiilor prime sau de tratare a diferitelor deşeuri poluante.

# În cadrul lucrării au fost puse în evidență posibilitățile practice pentru utilizarea instalațiilor cu microunde în cazul specific al decontaminării solurilor poluate cu produse petroliere. În acest scop a fost concepută o platformă pentru verificarea experimentală a eficienței procesului de decontaminare și a indicatorilor de proces.

# Datele obținute experimental au fost verificate pe baza simulării numerice a procesului, ceea ce a confirmat veridicitatea informațiilor obținute.

# De asemenea, au fost analizate aspectele energetice ale procesului de încălzire a solului poluat cu produse petroliere și a fost elaborată diagrama Sankey corespunzătoare.

# Analiza efectuată în cadrul lucrării a urmărit maximizarea puterii disipate în sol prin setarea sistemului de control pentru limitarea puterii reflectate.

# Dezvoltarea experimentului a impus elaborarea unei proceduri de planificare pentru a obține cele mai bune rezultate cu un număr minim de experiențe.

# Power Engineering Faculty

Contributions to the Development of Microwave Decontamination Methods for Polluted Environments

| PhD Student | PhD Advisor |
| --- | --- |
| Eng. Daniela IORDACHE | Prof. Nicolae GOLOVANOV, PhD |

# The intense preoccupations for protecting the environment and reducing the greenhouse gas emissions of the last decades have led to the development of environmentally “clean”, non-polluting decontamination technologies. The microwave technologies represent an important alternative due to their advantages in a large range of applications as compared to the traditional technologies, the best known being the processes of raw material processing or the treatment of different polluting wastes.

# The thesis underlines the possibilities to utilize the microwave installations in practice in the specific case of oil polluted soil decontamination. For this purpose a platform for the experimental verification of the decontamination process and process indicator efficiency has been developed.

# The experimentally obtained data have been verified by means of a numerical simulation of the process that has confirmed the accuracy of the obtained information.

# At the same time, the energy aspects characteristic of the heating process of the soil polluted by oil products have been analyzed and the corresponding Sankey diagram has been developed.

# The analysis carried out within the paper aimed at maximizing the power dissipated in the soil by setting the control system so that to limit the area of the reflected power.

# The experiments have required the development of a planning procedure in order to obtain the best results by means of a minimum number of tests.