UNIVERSITATEA POLITEHNICA DIN BUCUREŞTI

FACULTATEA DE INGINERIE ELECTRICĂ - DEPARTAMENTUL MĂSURĂRI, APARATE ELECTRICE ŞI CONVERTOARE STATICE

“CERCETĂRI PRIVIND SistemELE DE ACHIZIŢIE, monitorizare Şi avertizare A CALITĂŢII aerului În AREALE EXTINSe”

conducător de doctorat: Prof.dr.ing. Brânduşa Pantelimon

Doctorand: Ing. Andreea Cosac Voina

ABSTRACT

Prevenirea şi monitorizarea poluării atmosferice reprezintă probleme de interes public, naţional şi internaţional. O mare parte a problemelor de mediu actuale pot fi controlate sau diminuate prin dezvoltarea unor programe de monitorizare pe baza unor soluţii tehnico-ştiinţifice optime de măsurare şi cuantificare a indicatorilor de mediu specifici.

Ţinând cont că poluarea aerului înconjurător este una dintre cele mai dezbătute probleme din lume, teza de doctorat a propus o soluţie proprie pentru realizarea unui sistem de achiziţie şi monitorizare a calităţii aerului, funcţia principală a sistemului propus fiind de avertizare în timp real a factorilor de decizie în caz de poluare accidentală industrială şi o aplicaţie soft corespunzătoare. Pentru a evidenţia necesitatea realizării unui asemenea sistem, în lucrare s-a realizat şi un studiu de caz privind calitatea aerului în zona Dunării şi s-au identificat principalele surse potenţiale de poluare.

Aplicaţia soft propusă permite citirea, achiziţia şi monitorizarea semnalelor analogice, în caz particular tensiuni şi curenţi (semnale unificate 0...10V, 4...20mA), pentru analiza concentraţiilor poluanţilor principali ai aerului, programul permiţând şi semnalizarea optică şi acustică în momentul depăşirii valorilor limită impuse factorilor poluanţi. Tot în această aplicaţie, se permite vizualizarea şi reprezentarea grafică pe calculatorul la care este conectată placa de achiziţie, a variaţiilor semnalelor achiziţionate în timp real. De asemenea, aplicaţia afişează domeniile de măsură, limitele maxime admise, valorile medii, maxime şi minime la intervale prestabilite de timp pentru fiecare poluant monitorizat şi oferă posibilitatea de generare de rapoarte, transmiterea acestora la distanţă prin e-mail, precum şi trimiterea de e-mailuri de avertizare în cazul depăşirii valorilor limită admisibile pentru fiecare poluant în parte către factori de decizie, personal validare date, personal operator şi repetarea operaţiunii la interval de 1 oră dacă aceste valori nu au scazut sub pragurile de alertă. Datele achiziţionate în mod continuu sunt salvate automat într-o bază de date pentru a putea fi  trimise prin intermediul internetului la un dispecerat sau la un server în scopul analizei, prelucrării şi interpretării acestora. În urma acestor operaţiuni operatorul uman poate lua decizii corecte şi rapide cu privire la riscurile tehnologice apărute.

UNIVERSITY POLITEHNICA OF BUCHAREST

## Faculty of Electrical Engineering - Department of Measurements, Electrical devices and static converters

“RESEARCHes regarding ACQUISITION, MONITORING AND WARNING SYSTEMS OF AIR QUALITY IN EXTENDED AREAs”

Scientific coordinator: Prof.dr.eng. Brânduşa Pantelimon

PhD student: Eng. Andreea Cosac Voina

ABSTRACT

Prevention and monitoring of air pollution are issues of public, national and international interest. Much of the current environmental issues can be controlled or reduced through the development of monitoring programs based on the best scientific and technical solutions for measuring and quantifying the specific environmental indicators.

Taking into account that air pollution is one of the most debated issues in the world, the thesis proposed a solution for the development of a system for acquisition and monitoring of air quality and appropriate software application. The main function of the proposed system is real-time warning of decision factors in case of accidental industrial pollution. To highlight the need for such a system, in this paper was achieved also, a case study on air quality in the Danube area and have been identified the main potential sources of pollution.

The proposed software application allows reading, acquisition and monitoring of analog signals, voltages and currents in the particular case (unified signals 0 ... 10V, 4 ... 20mA) to analyze the concentrations of main air pollutants, the program enabling and optical and acoustic signaling when the pollutants exceed the admissible limits. Also this application allows the visualization and graphic representation of signals acquired in real time on the computer where is connected the acquisition board. The application also displays measuring range, maximum limits, mean, maximum and minimum values at preset time intervals for each pollutant monitored and allows the possibility of generating reports, sending them remotely by e-mail, and sending warning emails by decision makers, validation and operating personnel for each pollutant in part if allowable limit values ​​are exceeded and repeating after 1 hour if these values not decreased below the alert threshold. Continuously acquired data are automatically stored in a database to be sent via Internet to a central station or a server for analysis, processing and interpretation thereof. Following these operations the human operator can take fairly and expeditiously decisions on emerged technological risks.