Abstract (Ro)

Teza de doctorat are ca obiectiv general îmbunătăţirea performanţelor funcţionale ale unui motor sincron excitat cu magneţi permanenţi destinat acţionării directe a roţilor motoare ale unui vehicul. Obiectivul imediat al tezei este elaborarea unei propuneri de îmbunătăţire a performanţelor funcţionale ale unui motor sincron construit – numit motorul de bază.

Din analiza construcţiei motorului de bază, în ipoteza păstrării dimensiunilor de gabarit ale maşinii de bază şi a dimensiunilor pachetelor de tole, au rezultat posibilităţile de efectuare a următoarelor modificări constructive: modificări privind numărul de crestături pentru care este executată înfăşurarea trifazată a maşinii, modificări ale formei magneţilor permanenţi şi  modificări constructive ale pachetului statoric.

Pentru realizarea studiilor impuse de obiectivul imediat s-au elaborat modele parametrice 2D şi 3D, realizate cu programul profesional FLUX, care au fost validate prin compararea unor rezultate obţinute numeric şi experimental.

S-au efectuat trei studii: studiul privind efectul modificării numărului de crestături ale înfăşurării statorice asupra performanţelor maşinii de bază, studiul privind efectul unor modificări constructive ale magneţilor permanenţi şi studiul privind efectul unor modificări constructive ale pachetului statoric asupra valorii cuplului de agăţare şi asupra amplitudinii armonicii fundamentale a câmpului magnetic din întrefierul maşinii.

Pe baza studiilor efectuate s-au elaborat propuneri privind modificări constructive ale maşinii de bază în vederea creşterii performanţelor funcţionale.

Abstract (En)

The PhD thesis has as a general objective the improvement of the functional performance of a synchronous motor with permanent magnets designed for the direct drive of the wheels of a vehicle. The immediate objective of this work is to develop a proposal for improving the functional performance of a built synchronous motor – which is called a basic motor.

From analysing the construction of the basic motor, while taking into account the same overall dimensions of the machine base and the same lamination packet size, came up the possibility of making the following constructive changes: modifying the number of slots for the phase winding machine, changing the shape of the permanent magnets and implementing some constructive changes on the stator package.

In order to achieve the immediate objective, 2D and 3D parametric models were developed, by using the professional program called FLUX. These models were validated by comparing numerical and experimental results.

Three studies were made: a study regarding the effect of modifying the number of slots of the stator winding machine on the performance of the basic motor; another study took into account the impact of making structural changes of the permanent magnets; the last study analysed the consequences of making structural changes of the package stator on cogging torque and on the amplitude of harmonics in the air gap flux density machine.

Based on these studies a few proposals for construction changes of the basic motor were developed in order to increase its operational performance.