universitatea "politehnica" din Bucureşti

Facultatea de electrotehnică

Contribuţii la creşterea eficienţei sistemelor de măsurare în managementul sistemelor electroenergetice

Ing. Dan Apetrei

Datele obţinute din monitorizarea calităţii energiei electrice sunt incomplet utilizate în managementul sistemelor energetice. Dezvoltarea producţiei descentralizate de energie electrică folosind resurse regenerabile, principial necontrolabilă, face ca monitorizarea să nu mai fie suficientă. Trebuie dezvoltate sisteme de control a calităţii energiei electrice care să permită participarea la reglajul de sistem a noilor surse.

Contribuţii personale: conceperea, realizarea practică si analiza funcţionarii filtrelor de staţionaritate; realizarea practică a filtrelor diferenţiale de evenimente cu întârziere şi analiza comparativă a senzitivităţii; punerea la punct a algoritmului de grupare de tip clustering si parametrizarea acestuia în vederea detectării optime a evenimentelor; resincronizarea seturilor de date pe baza urmelor de evenimente; realizarea algoritmului de grupare a evenimentelor in vederea identificării de semnături; enunţarea principiilor de identificare a originii probabile a evenimentului pornind de la urmele de evenimente si echivalentul de transfer a perturbaţiei.

Cuvinte cheie: calitatea energiei electrice, urme de eveniment, clustering, staţionaritate

University "Politehnica" of  Bucharest

Power Engineering Faculty

Enhanced Power Quality Measurement for Management of Power Systems

By Dan Apetrei

Usability of data obtained from power quality monitoring could be enhanced. Renewables have a dramatic impact on power quality issues and is expected that monitoring won't be enough. That's why quality control systems would have to be developed. That means the new energy sources must be involved in the system stability control system.

The author's contributions are: practical determination of differential lagging filters sensitivity in finding events; practical stationarity analysis; clustering techniques development proving that Chebashev distance is effective in separation of event traces.

Keywords: power quality, event traces, clustering, stationarity